Interactive Activation and Competition Networks

---
How IACs work
- IAC’s consist of a collection of units.
- These units are gathered into competitive pools.
- Connections between different pools are excitatory.
- Connections within a pool are inhibitory.
- Excitatory connections are usually bi-directional.

---
- Within a pool, the inhibitory connections run from each unit within the pool to every other unit within the pool.
- This implements competition as the unit or units within the pool that receive the strongest activation tend to drive down the activation of the other units in that pool.
- Each unit has a continuous activation value between some max and min value.

---
- The activation value isn’t necessarily the same as the signal strength.
- We also have a threshold value, below which the activation signal is set to zero.
- This formula describes the net input to a unit i.
- Where extinput is some external input to the unit and noise is either zero or some random distribution.
sum from j w sub ij + extinput + noise(0,random)

---
- Note that we have some hyper parameters.
- Max and min.
- Decay
- Rest
if (net sub i > 0) newline %DELTA a sub i = ( max -a sub i )net sub i -decay( a sub i - rest ) newline else newline %DELTA a sub i = ( a sub i - min )net sub i - decay( a sub i - rest)

---
- Max and min are the activation maximum and minimum values. Normally max is set to one.
- Minimum is set to some value:
- min <= rest <= 0
- Decay is the rate at which units activation values return to zero if no new activation input is received, usually set to a value between zero and one.
  Note that the activation stays between max and min.

---
- Eventually, the activation of the unit will reach some equilibrium where the value stabilizes. This value is determined by the following:
- Setting rest to zero and max to one gives us the following:
a sub i = (( max )( net sub i ) + (rest)( decay )) over (net sub i + decay)
a sub i = ( (net sub i ) over ( net sub i + decay ))

---
- What that equation states is that the equilibrium of the unit is equal to the net input divided by the net input + the decay constant. (Assuming max = 1 and rest = 0).
- So, as the net input on a unit increases the activation value also increases, although the activation value never exceeds the max hyperparameter value.
- The decay hyper parameter is a restoring force that tends to bring the activation value back to the rest value (Again, usually 0).

---
- Note that if the net input is negative (i.e. inhibitory), the
  unit activation value becomes:
- This equation shows that inhibition is scaled by the absolute value of the minimum.
- Inhibition acts faster and drives the activation to lower level more quickly the farther that min is below zero.
a sub i = {abs(min)abs(net sub i ) } over {abs(net sub i ) + decay }

---
- But there’s more!
- We’ve talked about activation, now let’s discuss competition.
- Up until now, we’ve talked about fixed activation inputs.
- In this case, activation evolves to a fixed equilibrium point.
- But things get more complex. As units get input, they send that to other units in the pool as well.

---
- Units in the same pool are mutually inhibitory. This means that the unit with the highest inputs usually wins the day.
- Let’s take a look at the formulas for this. The y value is actually the greek symbol gamma.
- Let’s assume two units, a and b. The next slide shows the activation formulas for both.

---
- Here is the formula for the net input to unit a.
- Here is the formula for the net input to b.
- As long as the activations are positive values, we get the following:
net sub a = %epsilon sub a = %gamma( output sub b )
net sub b = %epsilon sub b - %gamma( output sub a )
net sub a = %epsilon sub a - %gamma sub b newline net sub b = %epsilon sub b - %gamma sub a

---
- Note that if the excitatory input to unit is larger than the one to unit b, than a’s inhibitory effect is larger on b than b’s is on a.
- This is the competition part of the network.
- A, getting a higher excitatory value, suppresses b by inhibiting it more strongly.
- Also known as “The rich get richer”.

---
- What if the effects of each unit on the other are equal?
- This leads to a state called “resonance”. In this state once one unit becomes active, it tends to make the other unit active as well.
- The two units are then sustained by the network and “resonate” in it.
- As an example, think of two sound frequencies resonating in a sound chamber.

---
- Let’s look at a concrete example...
- In this example we’ll set the activation value to 0.5 and set external inputs to zero (effectively removing them).
- Their activation values are twice the decay value.
- So, here we see that delta a is zero. I.e. no change.
%DELTA a sub i = (1 - a sub a)net sub a - (decay) sub a newline newline = (1 - 0.5)(2)(decay)(0.5) - decay(0.5) newline newline = (0.5)(2) decay(0.5) - decay(0.5) newline newline = 0

---
- This means that the IAC network can use the mutually excitatory connections between units in different pools to sustain input patterns that would normally decay away without continuous input.
- Note that these active units aren’t necessarily ones that are activated by external inputs. I.e. hidden units.

---
- Finally, the rate of evolution towards equilibrium in the network and even the actual equilibrium state that is reached is affected by the initial inputs.
- For example, forcing a specific unit to be ‘on’ can slow the activation of other units.
- In extreme cases, initially activating a unit can cause other units to never become active at all.
- This can be likened to a ‘dropout’ rate in neural network where formerly active nodes decay to zero.
- This is also known as “hysteresis”.

---
The IAC model architecture
- The architecture of IAC consists of the following components.
- Visible units. These are units to which external input can be applied.
- Hidden units. These are units to which no external input can be applied.
- Hidden units are only affected by net outputs from visible units.

---
The IAC model architecture
- IAC models have the following hyper parameters
  - max. The maximum activation value
  - min. The minimum activation value.
  - rest. The resting activation level which units settle to in the absence of any input.
  - decay. The rate of decay of activation values to return to their resting level.
  - estr. The strength of the external input.

---
The IAC model architecture
- IAC models have the following hyper parameters
  - alpha. Scales the strength of the excitatory input to other units.
  - gamma. Scales the strength of the inhibitory input to the other units.

---
The IAC model architecture
- Note that in the IAC model, these values apply globally to all units. Trying to apply individual hyperparameter values to each node becomes too complex to be feasible.
- The noise parameter is a separate value, which is usually included in the definition for the pool class.

---
The IAC model architecture
- The way these networks work is about pools and projections.
- A pool is a set of units
- A projection is a set of connections between the pools.
- All networks have a special pool called the bias pool.
- The bias pool is always the first pool. I.e. pool(1)

---
The IAC model architecture
- Projections are attached to units receiving connections from units in a different pool.
- The first projection is always the projection from the bias pool.
- The bias pool projection value can be any constant value.

---
The IAC core routines
- reset() - This routine resets the activation value of each unit back to its rest value. It also resets the cycle time to zero.
- cycle() - This routine is the main driver function. It carries out number of processing cycles. For each cycle, two routines are called getnet() and update().
- getnet() - Computes the net input for each pool. Note that net input consists of:
  - External input (estr)
  - Excitatory input from other units (scaled by alpha)
  - Inhibitory input from other units (scaled by gamma).

---
The IAC core routines
- For each pool, the getnet() routine first accumulates the excitatory and inhibitory inputs from other units, then scales the inputs and adds them to the scaled external input to obtain the net input.
- If the pool-specific noise parameter is non-zero, then it takes a random sample of a gaussian normal distribution and then this is multiplied by the net input value.
- Whether the net input is excitatory or inhibitory is determined by its sign. Positive net input is excitatory. Negative net input is inhibitory.

---
The IAC core routines
- The update() routine increments the activatin value of each unit, based on the net input and the existing activation value.
- Care should be taken to make sure that the new computed activation value doesn’t exceed either the max or the min hyper parameter value.